## Slide 1: Ice Control Chemicals
How ice control chemicals work
Brine
Slush
(Solution & Ice)
Solution
& Salt
Notes: This is the phase diagram for sodium chloride or rock salt. It shows the relationship between temperature (pavement) and the freezing point of various concentrations of salt brine.
POINT OUT SOME POINTS ON THE CURVE.
SHOW WHAT HAPPENS WITH TEMPERATURE TO A 15% SOLUTION
Salt must go into solution (brine) before it can melt any snow or ice. Keeping a Sufficient concentration of brine on the pavement surface must be maintained by periodic application in order to prevent refreeze.
Points of interest on this diagram include:
Eutectic temperature
Eutectic Concentration
The portion of the curve where freezing point increases with increasing solution concentration (similar to automobile radiator anti-freeze)

## Slide 2: Ice Control Chemicals
Sodium Chloride
Magnesium Chloride
Calcium Chloride
Notes: These are the phase diagrams for the 3 most common ice control chemicals. You will note that there is very little difference in the curves above a pavement temperature of 20 degrees F.
Point out the eutectic concentrations and temperatures for each chemical and that is meaningless to compare chemicals on that basis.
The only real difference is that calcium and magnesium chloride will melt ice more quickly, but they will basically melt no more ice per unit of chemical.

## Slide 3: Thoughts on Temperature
When we are using chemicals, we are only concerned with the pavement temperature!
The eutectic temperature (the low point of the V) is not the lowest effective working temperature of the chemical
Notes: Stress it again and again – you MUST know the pavement temperature – air temperature is not good enough. The melting has to happen at the pavement, so that is the place where we need to know the temperature.
Working temperatures – we will come back to this.